## Slide 1
Overall
- All relevant files are inside the folder named “Manual_design.zip”
Dropbox link for this folder is:
https://www.dropbox.com/s/qed8u9lidd9bj0c/Manual_design.zip?dl=0
- Manual size: A4 Tri-fold (Both Sided)
- Please make the look and feel similar to our existing product
package (Refer to file named “Existing-manual.pdf”)
- Please feel free to use any product images in the folder named “Product_photos.zip”
- The following slides are contents that need to be included in the manual.
I have left comments in blue colour
297 mm
210 mm
Flap
Back
Front
97 mm
100 mm
100 mm
A4 size into a tri-fold manual
Please use both sides of the space

## Slide 2
1. Features
Up to 3x water pressure
Patented watering plate with 412 photo-etched holes increase water pressure by 3 times.
Generates negative ions worth more than 100 waterfalls (Approx. 582,000 anions/cc)
Water passed through the patented super fine watering holes creates crazy amounts of negative ions that refreshes your body, plus purifies odours in the air.
Dual filtration system
1. Water filter: Removes contaminants and particles from water
2. Antibacterial ceramic filter: Helps kill bacteria and remove odour
Swirl-Action creates silky smooth water
Special wings attached to the ceramic filter creates a mini-tornado inside the handle.
This improves the filtration function and products silkier water with greater moisturising and massaging effects.

## Slide 3
2. Name of parts
Related image files are:
1. “Product-component-1.ai” 2. “Product-component-2.png”

## Slide 4
3. Installation
Remove the existing shower head by turning it anti-clockwise
Fit the drill-free bracket clockwise to the shower head outlet.
Tighten by hand only
Ensure that the bracket is
vertical and that the thread
faces straight down
Connect the hose to the shower head and to the bracket. The nut side of the hose should connect to the bracket. Make sure washers are placed inside the hose. Tighten by hand only
To adjust the position of the bracket holder, place the shower head onto the bracket and use it as a lever to swivel the holder up and down.
Related image files are:
1. “Installation1.jpg”
2. “Installation2.jpg”
3. “Installation3.jpg”
4. “Installation4.jpg”
5. “Installation5.jpg”

## Slide 5
1. Insert (D) Ceramic filter into (E) Handle. Make sure the propeller side of the Ceramic filter goes into the Handle first, facing downwards.
2. Insert (C) Water filter into (E) Handle. Make sure the fat end of the Water filter goes into the Handle first, facing downwards.
3. Place (H) Watering plate in the (I) Shower head cap. Make sure the side of the Watering plate with the engravings faces outwards (facing down on the table as in picture). Place the (G) White O-ring inside onto the Watering plate. Make sure the fat side of the White O-ring faces the Watering plate.
4. Screw (A) Shower head onto the (E) Handle. Screw (I) Shower head cap onto the Shower head. Make sure the (B) Top O-ring and
(F) Bottom O-ring are in the place properly. Missing or damaged
O-rings may cause leaks.
4. Shower Head Assembly
Instructions
These files are folder named:
“Assembly_photos.zip”
Related image files are:
1. “Assembly1.jpg”
2. “Assembly2.jpg”
3. “Assembly3.jpg”
4. “Assembly4.jpg”
5. “Assembly5.jpg”
6. “Assembly6.jpg”
7. “Assembly7.jpg”
8. “Assembly8.jpg”
9. “Assembly9.jpg”
10. “Assembly10.jpg”
11. “Assembly11.jpg”

## Slide 6
5. Maintenance
It is recommended that you regularly clean your shower head to prevent blockage and/or damages. Regular maintenance will also ensure optimal water pressure level. The frequency of your maintenance routine should vary depending on the quality of water in your location.
Because the photo-etched holes are very fine, lack of maintenance can cause build-up of lime, calcium and other particles in the holes. This can cause water pressure to exceed product specifications, leading to failures such as cracked parts, leaks, buckled shower plate, etc.
To correctly maintain your product, simply disassemble the shower head and follow the instructions below.
1. The ceramic filter is semi-permanent and will not need replacement if maintained correctly and if it is not damaged physically. Wash the ceramic filter under warm water and give it a good shake while rinsing to remove any build-up of dirt and other contaminants.
2. To clean the watering plate:
- Soak the watering plate in a bowl filled with white vinegar or fresh Coke
- Cover the bowl with plastic wrap
- Leave if for several hours, or overnight or longer if build-up is severe
- Minerals, lime, calcium and other build-ups will dissolve away from the holes
- Rinse the watering plate with cold water
3. Wash other parts of the shower head and assemble back together, making sure all the components are placed correctly. (See “Assembly Instructions” for detailed information)
4. The water filter can be replaced when dirty, or when the water pressure drops remarkably. Replacement cycles should vary depending on the amount of water consumed, water pressure, quality of the water in your location, etc. Average replacement cycle is once every 3 months.

## Slide 7
6. Important
Please read the manual before use, and follow the maintenance guidelines regularly to avoid possible damages or failures
Do not soak the shower head in water for a long time.
Do not use this product with hot water over 70℃.
Some metal pieces may have sharp edges. Please exercise care when assembling.
Gravity Fed users or users with under 100kpa water pressure in the region may not see improvements in their water pressure and/or may see fluctuations in the water temperature. Users with instantaneous hot water system may also see fluctuations in their water temperature.
7. Specifications
Materials: Heat-resistant PC
Recommended temperature: 0 ~ 70℃
Watering plate holes: Ø 0.20 / 412EA
Made in Korea

## Slide 8
8. Patents and Certifications
The image files for these 5 logos are in the file named “Logos.zip”

## Slide 9
9. Warranty
This warranty is limited to Quoss products purchased within the Commonwealth of Australia. Defects caused by improper care of the product or failure to observe any one or more of the installation instructions will not be covered by Quoss warranty. All warranty claims should be directed to Quoss. We do not assume any responsibility for errors/faults or any damages occurring from installation. Our warranty does not include any installation or uninstallation costs.
The Quoss warranty shall be void for the following reasons:
- Inability to provide proof of purchase or equivalent documentation
- Products not installed by relevant National Standards and State Regulations
- Products not installed/used in accordance with the manufacturer’s installation instructions
- Products used for incorrect applications
- Service repairs or with non-standard replacement parts previously undertaken without
written approval from Quoss
- Damage to product by accidently dropping during and or after installation
This product is warranted for 3 years from the date of purchase of the product. Use nonabrasive cleansers when you clean the shower head in order not to damage surface.
Warranty does not cover damage from incorrect cleaning practices.
Our goods come with guarantees that cannot be excluded under the Australian Consumer Law. You are entitled to a replacement or refund for a major failure and for compensation for any other reasonably foreseeable loss or damage. You are also entitled to have the goods repaired if the goods fail to be acceptable quality and the failure does not amount to a major failure.
Quoss product designs, functions and specifications are constantly updated. The information on this package may be out of date, inaccurate or incomplete to current Quoss lines when you access it.

## Slide 10
Customer Care Centre
1300 783 699
Qstore Pty Ltd
Unit 7, 9-11 South Street
Rydalmere 2116 NSW Australia
www.quoss.com.au
www.info@quoss.com.au
For company logo, please use file named “Quoss_logo.png”