## Slide 1: GCC OPERATIONAL TECHNOLOGY SECURITY FORUM & EXHIBITION 2017
Implementing A Comprehensive and Sustainable
ICS Security Framework

## Slide 2
What happens if the sign falls off?
SIGN SAYS: “Do not touch any of these wires”
Notes: Source: https://blog.dotcom-monitor.com/dotcom-monitor-news/server-cable-hell-15-of-the-worst-wiring-jobs-ever-2/

## Slide 3
Notes: Source:
https://www.lifewire.com/lag-on-computer-networks-and-online-817370

## Slide 4
Notes: SOURCE: https://www.geoilandgas.com/liquefied-natural-gas

## Slide 5
Notes: SOURCES: SANS ICS, TLP WHITE, Analysis of the Cyber Attack on Ukraine Power Grid, Defense Case, March 18, 2016
http://www.cbsnews.com/news/russian-hacks-into-ukraine-power-grids-may-be-a-sign-of-things-to-come/
http://cdn.powermag.com/wp-content/uploads/2016/05/PWR_050116_SR_Ukraine_Fig2.jpg,
http://cdn.powermag.com/wp-content/uploads/2016/05/PWR_050116_SR_Ukraine_Fig2.jpg
Capability
The attackers demonstrated a variety of capabilities, including spear phishing emails, variants of the BlackEnergy 3 malware, and the manipulation of Microsoft Office documents that contained the malware to gain a foothold into the Information Technology (IT) networks of the electricity companies.13 They demonstrated the capability to gain a foothold and harvest credentials and information to gain access to the ICS network. Additionally, the attackers showed expertise, not only in network connected infrastructure; such as Uninterruptable Power Supplies (UPSs), but also in operating the ICSs through supervisory control system; such as the Human Machine Interface (HMI) . Finally, the adversaries demonstrated the capability and willingness to target field devices at substations, write custom malicious firmware, and render the devices, such as serial-to-ethernet convertors, inoperable and unrecoverable.14 In one case, the attackers also used telephone systems to generate thousands of calls to the energy company’s call center to deny access to customers reporting outages. However, the strongest capability of the attackers was not in their choice of tools or in their expertise, but in their capability to perform long-term reconnaissance operations required to learn the environment and execute a highly synchronized, multistage, multisite attack.
The following is a consolidated list of the technical components used by the attackers, graphically depicted in Figure 3:
  Spear phishing to gain access to the business networks of the oblenergos
  Identification of BlackEnergy 3 at each of the impacted oblenergos
  Theft of credentials from the business networks
  The use of virtual private networks (VPNs) to enter the ICS network
  The use of existing remote access tools within the environment or issuing commands directly from a remote station similar to an operator HMI
  Serial-to-ethernet communications devices impacted at a firmware level15
  The use of a modified KillDisk to erase the master boot record of impacted organization systems as well as the targeted deletion of some logs16
  Utilizing UPS systems to impact connected load with a scheduled service outage
  Telephone denial-of-service attack on the call center

## Slide 6
What do I do now?
Where are my backups?
Which digital Forensic team should I call?
What is the number to QCERT?

## Slide 7
Notes: SOURCE: SANS ICS, TLP WHITE, Analysis of the Cyber Attack on Ukraine Power Grid, Defense Case, March 18, 2016
SOURCE: http://cdn.powermag.com/wp-content/uploads/2016/05/PWR_050116_SR_Ukraine_Fig2.jpg,
http://cdn.powermag.com/wp-content/uploads/2016/05/PWR_050116_SR_Ukraine_Fig2.jpg

## Slide 8
Notes: SOURCE: https://www.dmv.com/blog/insurance-doesnt-cover-all-winter-driving-hazards-523103

## Slide 9
Notes: SOURCE: http://images.dailytech.com/nimage/29707_large_distracted-driving.jpeg

## Slide 10
Notes: SOURCE: https://image.shutterstock.com/z/stock-photo-risk-management-diagram-business-concept-286960754.jpg

## Slide 11: We can not prevent cyber attacks 100%.
But we can reduce the chances to less than 100%.
Mitigations will define your resiliency and speed of recovery.
BUILDING A COMPREHENSIVE
AND SUSTAINABLE
SECURITY FRAMEWORK
PREVENT THE ATTACK
DETECT THE ATTACK
RESPOND & RECOVER

## Slide 12
Shutdown of plant processing
Destruction of the processing equipment
Disabling of safety functions
Financial Loss
Environmental impact
Safety incident
Unauthorized and Undetected control of ICS systems
Controlling and Monitoring the plant using Industrial Control systems
Notes: If you are worried about:
FADE TO GRAPHIC # 1: shutdown of plant processing – that may cause you financial loss
FADE TO GRAPHIC # 2: Destruction of the processing equipment – that may keep you from maintaining environmental control
FADE TO GRAPHIC # 3: Disabling of safety functions – that when needed, may not be available to safely control the plant
FADE TO GRAPHIC # 4: As a direct result of unauthorized and undetected control of your ICS systems;
FADE TO GRAPHIC # 5: which is a natural risk of using any industrial control systems to control and monitor the plant,
there are things we can do to prevent that top event. And this is where you ground all your preventive, detective and mitigative efforts. Understanding the possible causes and building your comprehensive security program. Along the way, you’re going to have to make choices as an Owner of what is acceptable and not acceptable risk.

## Slide 13
Unauthorized and Undetected control of ICS systems
Controlling and Monitoring the plant using Industrial Control systems
DIRECT PHYSICAL ACCESS
REMOTE CONNECTION TO THE SYSTEMS
MALICIOUS SOFTWARE
SYSTEM VULNERABILITIES
CYBER ATTACKS
Notes: But first things first, you must evaluate WHAT ARE THE WAYS THAT COULD POSSIBLY ALLOW UNAUTHORIZED AND UNDETECTED ACCESS TO YOUR SYSTEMS.
FADE TO GRAPHIC # 1: It could be PEOPLE who have direct physical access to the systems.
FADE TO GRAPHIC # 2: It could be FROM REMOTE CONNECTION TO YOUR SYSTEMS

## Slide 14
Unauthorized and Undetected control of ICS systems
Controlling and Monitoring the plant using Industrial Control systems
DIRECT PHYSICAL ACCESS
1
2
3
4
HEALTHY AND WORKING
NOT WORKING
IN PLACE BUT MODERATELY EFFECTIVE
NOT IN PLACE AT ALL
But, whap happens if these barriers fail?
What other controls do you have?
Notes: If it is through ,
FADE TO GRAPHIC # 1: DIRECT PHYSICAL ACCESS, What are the barriers in place to prevent such direct physical access from unauthorized individuals or groups?
NOTE: The shapes are merely placeholders. Please replace with the graphical depiction of your recommendation
FADE TO GRAPHIC # 2: Show the arrow disappearing and replace with a grahic representation of: PLANT SECURITY? Rectangle # 1
FADE TO GRAPHIC # 3: Show next to rectangular shape # 1 LOCKED ROOMS? Locked rooms is rectangular shape # 2
FADE TO GRAPHIC # 4: Show next to rectangular shape # 2 CCTV CAMERAS? CCTV cameras is rectangular shape # 3
FADE TO GRAPHIC # 5: Show next to rectangular shape # 3 SECURITY GUARDS? Security Guards rectangular shape # 4
And are they in place today AND IN GOOD STATUS? Show the different graphics changing colors from GREEN (in place and healthy), RED (in place but not healthy), YELLOW (in place but moderately effective or have some issues) AND BLACK (not in place)
FADE OUT ALL TEXT: HEALTHY AND WORKING, NOT WORKING, IN PLACE BUT MODERATELY EFFECTIVE, NOT IN PLACE AT ALL
AND, if all these barriers fail,
SHOW ALL PREVIOUS GRAPHICS OF THESE BARRIERS FAILING ONE, BY ONE, What controls are left in place?

## Slide 15
Unauthorized and Undetected control of ICS systems
Controlling and Monitoring the plant using Industrial Control systems
DIRECT PHYSICAL ACCESS
Notes: Then the unauthorized individual gains control of your ICS Systems. Especially if these systems are unamanned.
FADE TO GRAPHIC # 1: Show a graphic of individual gaining unauthorized access to the system.
BUT IS THAT TRUE?
AREN’T THERE ANY OTHER CONTROLS WITHIN THE SYSTEMS THEMSELVES THAT PREVENT THE ACCESS ALTOGETHER?

## Slide 16
COMPUTER
Login name:
Password:
Administrator
DeltaVAdmin
Fox
Gnomes
Maint
Tech
“Password”
“Admin”
“qatar2017”
“IloveQatar”
Audit Trails
Password required
Password length
USB
Notes: FADE TO GRAPHIC # 1: Show graphic of a computer.
FADE TO GRAPHIC # 2: Show graphic depicting LOGIN NAME AND PASSWORD What about the login name and password? Isn’t that some form of a barrier to to control direct unauthorized access?
But as long as the passwords are not:
Default, FADE TO GRAPHIC # 3: Show the text “ADMINISTRATOR”, followed by a series of TEXT GRAPHICS without any pauses (one after another) then make them all disappear in the end.
“DeltaVAdmin:
“Fox”
“Gnomes”
Or Generic, FADE TO GRAPHIC # 4, : Show the the following series of TEXT GRAPHICS without any pauses (one after another) then make them all disappear in the end.
“Maint”
“Tech”
And the passwords are not easy to guess. FADE TO GRAPHIC # 5: Show the the following series of TEXT GRAPHICS without any pauses (one after another) then make them all disappear in the end.
“Password”
“Admin”
“Qatar2017”
“ILoveQatar”
Then you should be okay. But what if you have not done the job of hardening these systems, and security policy settings such as:
FADE TO GRAPHIC # 6: Show the GRAPHIC rendition of the following objects without any pauses (one after another) then make them all disappear in the end.
“Audit trails”
“Password required”
“Password length”
“etc.
Have not even been set? Have you conducted an access review of your user ID’s and passwords? Do you know which users are suppoed to have what access? When was the last time you did a clean-up of your ID’s and passwords? Do you even have a policy that defines access management?
Many things can go wrong when you have direct physical access to that computer. For example, you can insert an infected USB and introduce a virus.
FADE TO GRAPHIC # 7: Show a graphic of a person walking up to a computer, inserting a USB stick and the computer getting infected and the infection spreading to the other computers in the network and fade it out completely.
Do you have REMOVABLE MEDIA controls in place? Do you even have policies that define how to control and manage these things? What about the laptop that the vendors use to connect to your systems? Do you have a process in place to manage them?

## Slide 17
“Is the situation active? Then control it. Contain the spread”
“If not active, commence situation analysis.”
“Extract audit logs. Preserve the evidence.”
“Is situation under control? Then start recovery.”
“Backups, Spare hardware, Software media, Software license, etc. ”
“Communicate and report the incident to appropriate individuals, groups, authorities.”
Business Continuity Plan /Disaster Recovery Plan
Notes: And if you do get infected, Do you then have the team to respond to incidents like these that know what to do?
FADE TO GRAPHIC # 1: Show a graphic rendition of a team responding to computer emergency and label this team Response Team. Start streaming and super imposing the following words on the Powerpoint as the response team is shown.
“Is the incident active? Then control it – contain the spread.”
“if not active, commence situation analysis
“Extract audit logs. Preserve the evidence”
“Backups, S[are hardware, Software media, Software license, etc.
“Communicate and report the incident to appropriate individuals, groups, authorities”.
FADE TO GRAPHIC # 2: If you haven’t quite figured it out, you will not only need a response team, but also the contingency and recovery plans in place - BCP/DRP (Business Continuity Planning and Disaster Recovery Planning).
Do all these things prevent the direct physical access altogether? It does not, BUT, it will define the THE SPEED OF YOUR RECOVERY.

## Slide 18
Notes: I’d like to think that local and internal threats are the only thing that keeps me up at night, but unfortunately and realistically, most of our ICS network also have connectivity to:
FADE TO GRAPHIC # 1; The Business network where we pass plant information data for production allocation purposes and predictive analysis.
Show remote connectivity to the Corporate IT network Depict this by animating the following: Flow, Level and Temperature readings coming from valves, motors and pumps, traversing Industrial control systems network, to a computer user in the Corporate IT network.
FADE GRAPHIC # 1 and then SHOW next GRAPHIC # 2
FADE TO GRAPHIC # 2: The vendors who connect to our control systems to extract machine data.
Show remote connectivity by a vendor. Depict this by showing a vendor from the internet connecting to the a computer from within the Industrial Control Systems Network and call this computer a DATA SERVER.
But if you haven’t mapped out the boundaries of your network and your network drawings are not maintained, how are you able to identify weaknesses and vulnerabilities in the architecture?
Have you evaluated whether your systems are properly segregated? Do you have firewalls and switches in place and have they been properly configured? Do you even conduct a periodic access review of your firewalls and switches? Do you even have an equipment inventory?
And when it comes to external connection, if you can avoid it – AVOID IT ALTOGETHER. But if you can’t avoid it, then evaluate what’s the true need from the vendor. Are they needing just data or real time access? If data is the only thing they need, perhaps we can provision that data somewhere in the Corporate DMZ where they can extract it.
SHOW A GRAPHIC OF DATA FLOW FROM THE L1 LEVEL ENDING UP IN A SERVER IN THE CORPORATE DMZ AND THE THIRD PARTY VENDOR REACHING OUT TO GET TO THIS DATA .
For example, you can install a DATA DIODE – FADE TO GRAPHIC OF A DATA DIODE APPEARING; REPLACING THE ICS FIREWAL
The more important thing you need to ask yourself is, do you have a policy or work practice that defines ALL these standards and requirements?
NOTE: The powerpoint slide depicting this narrative is a sample only. I would like for you to make this graphic even more pizzazz and to animate appearances of certain objects per the script above.

## Slide 19
Notes: So far, I spoke about
Physical security FADE TO GRAPHIC # 1: Depict this by super imposing in the existing diagram that L3.5, L3, L2 and L1 network levels, a sort of a perimeter that indicates they are enclosed in a badge accessible room (animate)
Electronic security FADE TO GRAPHIC # 2: Depict this by super imposing in the existing diagram picture of a LOCK appearing next to all SERVERS, FIREWALLS, WORK STATIONS, in L3.5, L3, L2 and L1 (animate).
AND, External and Remote Connection security FADE TO GRAPHIC # 3: Depict this by animating the RED LINE coming from the vendor and ending up in the OPERATOR CONSOLE in the L2 level and then showing an X symbol on the line itself, next to the OPERATOR CONSOLE.
You’ve evaluated the physical security installed in your facilities. FADE TO GRAPHIC # 4: Depict this showing /animating components of electronic badge access systems, CCTV cameras, being installed.
You’ve hardened your ICS equipment – removed all Administrative, and Default passwords, re-structured the user access assignments, configured all security policies, disabled USB access. FADE TO GRAPHIC # 5: Depict this by animating a person logging in with Administrator and unable to do it, and inserting USB stick and unable to do it.
Segregated your networks – placed network control points, Data Diodes, Firewalls, Switches and Routers and tightened the configurations. FADE TO GRAPHIC # 6: Depict this by emphasizing/animating the ICS FIREWALL appearing between L3.5 and the IT FIREWALL, and doing the same animation with the ROUTER between L3.5 and L3, and the SWITCH between L3 and L2 networks.
Secured the remote access by vendor. FADE TO GRAPHIC # 7: Depict this by animating a vendor logging in from the Third Party Vendor site and unable to access the systems
You felt that you have done a good job in cleaning and securing the environment, FADE TO GRAPHIC # 8. Depict this by animating a person feeling pretty content about the good work he has done.
but as we know, PEOPLE are the weakest link in the chain and TRUST is not an acceptable security model, FADE TO GRAPHIC # 9: Depict this by animating a picture of a person doing malicious things with their Admin access and hiding their work by later erasing the log of their activities. Then super-impose a chain breaking then fade out graphics.
so how do we know what is happening in this environment if we don’t have the feedback mechanism in place? FADE TO GRAPHIC # 10: Depict this by animating some kind of a report spitting out a continuous list of security violations then fade out.
In addition, what kind of mechanism do we have in place to let us know whether the security configurations you put in place 3 months ago are still in place and functioning? This is where you build in the capabilities to detect and monitor the state of security of your environment
But how do we accomplish that objective, in a fool-proof, air tight, process without the subjectivity and bias of human judgment? This is where the checks and balances of technology and procedural controls come into place.

## Slide 20
Intrusion Detection / Prevention System
SIEM
Network Monitoring System
Privileged ID Mgt. System
Notes: If you build in the functionalities like:
FADE TO GRAPHIC # 1: Intrusion Detection Systems and Intrusion Prevention Systems – you will be able to detect intrusions and allow you to respond in a time critical manner
FADE TO GRAPHIC # 2: Security Incident Event Monitoring – you will have be notified the minute a suspicious activity emerges and which of the Administrators did what
FADE TO GRAPHIC # 3: Privileged ID Management Systems – you will be able to control the use of powerful ID’s and enforce pre-authorization for those usage
FADE TO GRAPHIC # 4: Network Monitoring systems – you will have the capabilities to monitor your network and detect rogue connections real time.
With just these basic functionalities, you have significantly reduced the probabilities of a successful attack and increased your probabilities for averting a cyber incident. Without the power of MONITORING and DETECTION, you are running blind and exactly the type of environment a hacker would take advantage of. Cyber incidents are not always about loud explosions it is also about the silent, invisible adversary, waiting for the right moment to bring your operations to a halt. The worth of 1 day’s production loss is the minimum risk you are taking, in a worst case scenario, this 1 day can easily turn into weeks. In a worst case scenario, somebody may get hurt. You have to ask yourself “can you afford it?”
But why put ourselves in a position to detect just when events happen? There are many things that we can measure and track that can give us indication whether the security health of our environment is slowly degrading. Malcolm Gladwell described ithe Tipping Point phenomenon whereby “the sum of many small things drives toward making a notable massive difference in outcomes”. Imagine if we do not manage these labor intensive and seemingly low value small things and nobody really care to track, for example, things like antivirus updates, patch applications, and access review?

## Slide 21
Shutdown of plant processing
Destruction of the processing equipment
Disabling of safety functions
Financial Loss
Environmental impact
Safety incident
Unauthorized and Undetected control of ICS systems
Controlling and Monitoring the plant using Industrial Control systems
DIRECT PHYSICAL ACCESS
REMOTE CONNECTION TO THE SYSTEMS
MALICIOUS SOFTWARE
SYSTEM VULNERABILITIES
CYBER ATTACKS
Antivirus Application
Patch
Management
Security Configuration
Management
Firewall Management
Notes: Then imagine each one of the barriers that separate us from the threats to the preventing the top event falling one by one, until the very thing we fear, which is unauthorized and undetected control of ICS systems, comes to fruition?
NOTE TO THE GRAPHIC DESIGNER: Please view this slide in Presentation mode. This is a conceptual depiction of the barriers of control that first appeared in Slide 12. You can remain consistent with that representation. However, I would like to animate each of the horizontal bar (i.e. Firewall Management, etc.) show as a barrier that is preventing us from reaching the top event, as failing one by one. I leave it to your imagination to represent this in the most dramatic way that captures the viewers interest.

## Slide 22: Industrial Control System Security
PLANT
PROCESS
(Level 0)
External Perimeter Defense
(Level 3.5)
Physical Security
Main Gate Security
Qatargas Security
ITR, Sub station, etc. Badge access
Electronic Security
System hardening (access controls)
Data Diodes
Firewalls, Routers
Intrusion Detection
Intrusion Monitoring
Malware protection
Patch Management system
Backup and restore system
Privileged ID Management
ICS Network Border Security
(Level 3)
Physical Security
ITR , Sub station, etc. Badge access
Electronic Security
System hardening (access controls)
Firewalls, Switches
Malware protection
Patch Management system
Backup and restore system
Privileged ID Management system
1
2
3
HMI and Work Station Security (Level 2)
Physical Security
ITR , Sub station, etc. Badge access
Electronic Security
System Hardening (access controls)
Firewalls, Switches
Malware protection
Patch Management system
Backup and restore system
Privileged ID Management system
4
Controller Level Security (Level 1)
Physical Security
Main Gate Security
Qatargas Security
Electronic Security
System hardening (access controls)
Controller Firewall
Secure laptop
Backup and restore system
Procedural Controls
Risk Assessment, Third Party Access Management, Project Security, User Access Management, Removable media , Access Reviews, etc.
PLANT
PROCESS
(Level 0)
Notes: Security is about building in the layers of defense. If you can imagine the famous “onion ring” analogy, every single layer of this onion is a layer that protects the core, then you can imagine that to protect your core process means visualizing what preventive, detective security you can put in place to prevent the adversary from reaching the prize. And, if the worse thing happens, the mitigative controls to swiftly recover.
The last man standing is the only man that can imagine the worst case scenario, prepare for that scenario and make risk decisions to accept and not accept certain consequences. Building the most comprehensive security program requires building a robust architecture, having the strategy to secure each layer, the work practices to develop a culture of security that hopefully will become second skin to all, and finally, the technology to prevent, detect and recover.
NOTE TO THE GRAPHIC DESIGNER:
Please view this slide in presentation mode. The idea behind this graphic animation/depiction was to show that there are layers between the process and the threats that endanger the security of the plant process. Having the layers of defense, as shown here, is like an “onion” that if each layers fail, the core is exposed. Therefore, I would like to show the same “onion” analogy with the same 1, 2, 3, 4 layers of defense as this presentation depicts fall one by one and what happens when the core is reached (boom, an explosion perhaps?) but in a more “dramatic” way. I leave it to your imagination to depict this in the most impressive way without losing the “onion” analogy and layers of defense message.

## Slide 23: Establishing an ICS Security Framework
Step # 1: Gain Management’s support
  Identify the Program Owner, Program Custodian, Policy Owner, ICS Equipment Owner and Custodians
Step # 2: Develop an ICS specific security policy
Step # 3: Establish the team
Step # 4: Develop the plan and resourcing
Step # 5: Execute the plan
  Phase 1: Scope
  Phase 2: Implement
  Phase 3: Sustain
Notes: So how does one do it? Security does not make you more barrels of oil, but it prevents you from losing all of it, so the first step is
FADE TO GRAPHIC # 1: Gain Management’s Support.
Depict this by animating Management acknowledging the creation of Industrial Control Systems Security Program for the company.
FADE TO GRAPHIC # 2: Develop the organization’s security policy
Depict this by animating the creation of the Industrial Control Systems Security Policy
FADE TO GRAPHIC # 3: Establish the team
Depict this by animating the creation of an ICS Security specific team. Show the team members having the proper qualifications/certifications like GICSP, CISSP, CISM, etc.
FADE TO GRAPHIC # 4: Develop the plan and resourcing.
Depict this by animating the creationgof a 5-year plan with resources and budget.
FADE TO GRAPHIC # 5: Execute the plan
Depict this by animating a 5-year plan showing the cycles of doing the scoping in a process plant, implementing the security program and sustaining it.

## Slide 24
ICS Security Program
Inventory
Map
ICS Security Program Implementation, and Sustainment Life Cycle
Assess
3. Risk Assess / Gap Assess
Address
Address
4.Counter
5. Train
Manage
Manage
9. Mitigate
8. Prevent
7. Detect
Sustain
Sustain
10. Steward
11. Verify
12. Evolve
Notes: Security is a life time program. As long as your plant is running, there is a prize to secure, but where do you start?
FADE TO GRAPHIC SET # 1: Assess your current environment. Show the ASSESS word
Note to the Graphic Designer: Please show the following elements one at a time, fading it in on-click.
Inventory your ICS environment - animate the act of collecting data and storing it in a database, then fade out. Flash in the screen a list of equipment inventory (set the animation to click on fade out). See slide 26 for the list. However best you can represent this .
Leave the words INVENTORY in place after fading out.
Map the boundaries of your ICS environment – animate the act of drafting a network diagram, then same as the one above, fade the scene but leave the words in place (MAP ).
Conduct an ICS Security Risk Assessment and a Gap Assessment against your own ICS Security Policies –animate this by showing a group of people meeting and discussing SCADA systems – super impose the words Initial Risk, Residual Risk, Threats, Probabilities+Consequence. Then do the same as above.
FADE TO GRAPHIC SET # 2: Address the gaps identified in the assessments. Show the ADDRESS word
Note to the Graphic Designer: Please show the following elements one at a time, fading it in.
Put the countermeasures in place – animate a person securing the ICS environment, going PC by PC and configuring security policies, then fade out the graphic but leave the word, COUNTER in place.
Train and Educate the people – animate a group of people being trained and then fade out the graphic but leave the word, TRAIN in place.
FADE TO GRAPHIC SET # 3: Manage and monitor the environment. Show the MANAGE word.
Note to the Graphic Designer: Please fade in the words PREVENT, DETECT AND MITIGATE one after another without pause, then…..
Animate elements of INTRUSION DETECTION SYSTEMS, SECURITY INCIDENT AND EVENT MONITORING, NETWORK MONITORING SYSTEMS in series then fade these elements out but leave the WORDS PREVENT, DETECT AND MITIGATE in place.
FADE TO GRAPHIC SET # 3: Sustain the program. Show the SUSTAIN word.
Note to the Graphic Designer: Please show the following elements one at a time, fading it in.
Steward and report on the health of your security program – animate a person reporting security metrics and KPI’s to Management. Fade out scene but leave the word STEWARD in place.
Verify and assess whether controls are still n place and working – animate a person checking whether the security policies he applied in the PC is still in place. Fade out scene but leave the word VERIFY in place.
Evolve. Be sensitive to the changes in security landscape – animate a person checking the security bulletins and taking action to make changes in the computer based on Threat report. Fade out scene but leave the word EVOLVE in place.

## Slide 25: SUPPORTING SLIDES

## Slide 26
ICS Equipment